## Slide 1: Digital System

## Slide 2: Digital Signal Representation
High Precision – Higher number of bits required
Notes: Byte – 8 bits, a standard now since 1956!
Bit
12-bit, 20-bit were also present

## Slide 3: Digital Signal Representation
Binary digit represents – logic HIGH or logic LOW
In an electronic system – logic HIGH is 1, logic LOW is 0 or vice-versa
1 bit represents – 2 states
2 bits represents – 4 states – {00,01,10,11}
n bits represents – 2n states
210 = 1024 ~ 1K bits
220 = 10,48,576 ~ 1M bits

## Slide 4: Analog and Digital Systems
Analog systems process analog signals which can take any value within a range
  Microphone, Analog meter display
Digital systems process digital signals which can take only a limited number of values between two values
  Flip-flops, Shift registers, Digital display

## Slide 5: Advantage and Disadvantages of Digital Systems
High accuracy (+)
Programmability (+)
Maintainability (+)
Design Automation (+)
Area, Power, Performance (-)

## Slide 6: Introduction
Rise in functionality increase design complexity
  So, post design steps are automated using Computer Aided Design (CAD) tools
    However, even designs using automated CAD tools may have bugs
  Due to extremely large size of the design space it is not possible to verify correctness of the design under all possible situations
  Techniques that can verify, without exercising exhaustive input-output combinations, that the design meets all the input specifications - formal verification

## Slide 7: Introduction
Manufacturing defect could arise due to decrease in the inter-component distance
All the chips need to be physically tested by giving input signals from a pattern generator and comparing responses using a logic analyzer - testing.
In the process of manufacturing a VLSI IC there are three broad steps
  Design
  Verification
  Test
Categorization of the IC’s can be done based on the functionality
  Analog, Digital or Mixed-signal
Analog IC
  Ex: Current mirrors, Voltage followers, filters, OPAMPs etc. work by processing continuous signals.
  They perform functions like amplification, active filtering, demodulation etc.
Digital IC
  Ex: logic gates, flip-flops, multiplexers, and other circuits which work using binary mathematics to process "one" and "zero" signals.
Mixed Signal IC
  Ex: Analog to Digital Converter (ADC)

## Slide 8: Introduction
Automation algorithms and CAD tools are mainly available for digital ICs
  Digital circuits comprise millions of components and transformation of design specifications to silicon implementation can be accomplished using logical procedures
Most of the analog circuits comprise less than hundred devices and its design is like an “art” which is best performed by designers with “aid” of some CAD tools

## Slide 9
Introduction

## Slide 10: Design Abstraction Levels
n+
n+
S
G
D
+
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
Introduction

## Slide 11
Introduction

## Slide 12
Introduction
F=AB+C
Architecture
Components
Gates
Transistors
Layout
IC
Top-down design - Design complex circuits in a simple way
Bottom-up analysis – Analyze simple components in a complex way

## Slide 13: Introduction
Functionality of electronics equipment and gadgets has increased but their physical size has come down drastically
  Due to the rapid advances in integration technologies - millions of transistors in a single Integrated Circuit (IC) or chip.
Small Scale Integration (SSI) - integration with 10's of transistors
Medium Scale Integration (MSI) - integration with 100's of transistors
Large Scale Integration (LSI) - integration with 1000's of transistors
Very Large Scale Integration (VLSI) - integration with 1000's of transistors